## Slide 1
SMART PLANT HEALTH MONITORING & AUTOMATIC IRRIGATION
MDP Project Proposal
ESP32 • Sensors • Automated Watering • Plant Health Insights
1

## Slide 2
1. Problem Statement
Why is smart irrigation needed?
Overwatering
Too much water can damage roots, waste resources and increase the risk of fungal problems.
Underwatering
Plants may become stressed when watering is based only on a fixed schedule.
No Continuous Feedback
Manual monitoring does not provide continuous information about soil and environmental conditions.
2

## Slide 3
2. Proposed Solution
A closed-loop system that measures, decides and acts automatically.
SENSE
Soil moisture Temperature Humidity
DECIDE
ESP32 compares readings with limits
ACT
Pump turns ON/OFF as required
INFORM
Display / mobile status & alerts
Core idea: water the plant only when the measured conditions indicate that watering is needed.
3

## Slide 4
3. System Architecture
Main hardware and information flow
ESP32 Microcontroller
Reads sensors • Runs decision logic • Controls pump
Soil Moisture Sensor
Measures water level in the soil.
DHT22 / Similar
Temperature + relative humidity.
Optional Sensors
Light, rain, water level, etc.
Relay / MOSFET Driver
Provides safe switching for the pump.
Water Pump
Delivers water through tubing.
Dashboard / Display
Shows readings and system status.
4

## Slide 5
4. Key Components
Suggested components for the prototype
ESP32
Main controller; Wi‑Fi/Bluetooth enabled.
Capacitive Soil Moisture Sensor
More suitable for repeated soil monitoring than basic resistive probes.
DHT22 / BME280
Temperature and humidity measurement.
Mini DC Water Pump
Moves water from a reservoir to the plant.
Relay Module / MOSFET
Interfaces the ESP32 with the pump.
Power Supply
Separate suitable supply for pump and controller; common ground where appropriate.
5

## Slide 6
5. Team Roles & Responsibilities
How Mechatronics, ECE and CSE members contribute to one integrated system
MECHATRONICS
• Plant setup and physical system design • Water tank, tubing and pump arrangement • Mechanical mounting / enclosure • Irrigation mechanism and flow testing • Physical integration and reliability testing
ECE
• ESP32 hardware and interfacing • Soil moisture, temperature & humidity sensors • Signal reading and calibration • Relay / MOSFET driver for pump control • Power supply, wiring and embedded firmware
CSE
• Website / web dashboard • Live sensor-data display • Manual pump ON/OFF control • Data storage and visualization • Backend/API, alerts and future analytics
All three teams collaborate during system integration, testing and final demonstration.
6

## Slide 7
6. Web-Based Monitoring & Manual Irrigation
The user can monitor the plant remotely and also control watering when required.
Smart Plant Dashboard
Soil Moisture
32 %
Temperature
28 °C
Humidity
61 %
Irrigation Control
PUMP ON
PUMP OFF
Last watering: 12:42 PM • Pump status: OFF
LIVE MONITORING
View soil moisture, temperature, humidity and pump status.
MANUAL CONTROL
User can press PUMP ON/OFF from the website when manual watering is needed.
AUTOMATIC MODE
The system normally makes the watering decision automatically using sensor data.
7

## Slide 8
7. Control Logic
Simple decision-making is enough for the first working prototype.
Read
Get soil moisture, temperature and humidity.
Check
Is soil moisture below the chosen threshold?
Water
If dry → activate pump for a short, fixed duration.
Wait & Recheck
Allow water to distribute, then measure again.
Protect
Stop watering if reservoir is empty or another safety condition occurs.
8

## Slide 9
8. Example Operating Cycle
Illustrative behaviour of the prototype
SOIL DRY
Moisture below threshold
PUMP ON
Water for e.g. 5–10 s
SOIL RECOVERS
Wait and stabilize
PUMP OFF
Continue monitoring
Important: the moisture threshold and pump duration should be calibrated experimentally for the selected plant, soil and pot.
9

## Slide 10
9. Software & User Interface
From sensor readings to useful plant information
ESP32 Firmware
• Sensor reading • Threshold comparison • Pump control • Timing & safety checks • Serial monitoring
Data / Connectivity
Option A: local OLED/LCD Option B: Wi‑Fi dashboard Possible data: moisture %, temperature, humidity, pump status, last watering time
Alerts & Insights
• Low water level • Very dry soil • Abnormal sensor values • Daily watering count • Historical trends
10

## Slide 11
10. What Makes This a Strong MDP Project?
The project can go beyond a basic automatic plant waterer.
Embedded Systems
Real-time sensor acquisition and actuator control.
IoT
ESP32 enables remote monitoring and data logging.
Automation
Closed-loop control reduces unnecessary watering.
Data Analysis
Use trends to study plant/environment conditions.
Engineering Design
Requires hardware integration, power management and calibration.
Scalability
Can be extended from one plant to multiple plants/zones.
11

## Slide 12
11. Possible Enhancements
Features that can raise the project from a prototype to a stronger MDP.
Water-Level Sensor
Prevent dry-running the pump.
Light Sensor
Relate plant conditions to available light.
Rain Sensor
Avoid unnecessary outdoor watering.
Multiple Plant Zones
Different moisture thresholds for different plants.
Mobile/Web Dashboard
View live readings and control modes.
Prediction / Smart Scheduling
Use historical data to improve watering decisions.
12

## Slide 13
12. Development Roadmap
Build the project in stages so a working prototype comes early.
Phase 1
ESP32 + soil moisture sensor
Read and calibrate moisture values.
Phase 2
Add pump + driver
Implement automatic ON/OFF control.
Phase 3
Add temperature/humidity
Log environmental conditions.
Phase 4
Dashboard / display
Show live data and watering status.
Phase 5
Testing & calibration
Compare watering strategies and refine thresholds.
Phase 6
Final demo
Package hardware, enclosure, documentation and results.
13

## Slide 14
THANK YOU
Smart irrigation is not just about watering plants.
It is about using data to make better decisions.
14